## Slide 1
Machine Vision
Wu Wei

## Slide 2
01
Arithmetic/Logical Operation
Gray Level Transformations
Histogram Processing
Images Enhancement
02
03
Spatial Filtering
04
Frequency Filtering
05

## Slide 3
principle objective of Image enhancement
Image Enhancement
  To process an image so that the result is more suitable than the original image for a specific application.
  specific: Problem Oriented
    Highlighting interesting detail in images
    Removing noise from images
    Making images more visually appealing
    De-emphasizing things in an image
    Finding things in an image
    ……

## Slide 4
Categories of image enhancement approaches
Image Enhancement
Spatial Domain Methods
  The image plane itself
Direct manipulation of pixels in an image
  Frequency Domain Methods
Consider the image as a 2D signal and apply Fourier transform
Process the image in the transformed domain
Apply the inverse transform to return into the spatial domain.
No general theory of image enhancement
“good image” is an elusive standard for visual evaluation

## Slide 5
PART 1
Gray Level Transformations

## Slide 6
Basics
Image Enhancement
Intensity transformation and spatial filtering
g (x, y) = T[ f (x, y)]
f (x, y) : input image g (x, y) : output image T : an operator applied to the image f (x, y)
In the discrete case
• f and g are 2D matrices of size W × H
T is a matrix of size w × h which is much smaller than W × H
The value of each pixel of g is the result of applying the operator T at the corresponding location in f.
If w × h= 1×1 →intensity transform
Otherwise, it’s spatial filtering.
Origin
x
y
Image f (x, y)
(x, y)

## Slide 7
Basic Gray Level Transformations
Image Enhancement
The simplest spatial domain operations occur when the neighbourhood is simply the pixel itself
In this case Point processing operations take the form
s = T ( r )
T : a grey level transformation function or a point processing operation
s : processed image pixel value r : original image pixel value

## Slide 8
Basic Gray Level Transformations
Image Enhancement
Examples
Image negatives
Log transformations
Power-law (Gamma) transformations
In the following
Each image is represented with a 2D matrix of L intensity levels. That is each pixel takes a value between 0 and L-1

## Slide 9
Basic Gray Level Transformations
Image Enhancement
Threshold function
Contrast stretching
Produce an image of higher contrast by darkening the levels below k and brightening the levels above k in the original image, known as contrast stretching.
In the limiting case, T(r) produces a two-level (binary) image, known as thresholding.

## Slide 10
Basic Gray Level Transformations
Image Enhancement

## Slide 11
Basic Gray Level Transformations
Image Enhancement
Thresholding transformations are useful for segmentation in which we want to isolate/emphasize an object of interest from a background
Result called “BINARY” image.
Original image
Thresholding transformation
s =
255, r≥ threshold
0, r ＜ threshold

## Slide 12
Image negatives
Log transformations
Power-law (Gamma) transformations
Piecewise Linear Transformation
Basic Gray Level Transformations

## Slide 13
Basic Gray Level Transformations
Input gray level r
Output gray level s
0
L/2
L-1
L-1
L/2
negative
original
Negative transformation
s = L – 1 - r
It is particularly suited for enhancing white or gray detail embedded in dark regions of an image, especially when the black areas are dominant in size
Original image
Negative transformation

## Slide 14
Basic Gray Level Transformations
Negative transformation

## Slide 15
Image negatives
Log transformations
Power-law (Gamma) transformations
Piecewise Linear Transformation
Basic Gray Level Transformations

## Slide 16
Basic Gray Level Transformations
s = c · log(1 + r)
Input gray level r
Output gray level s
0
L/2
L-1
L-1
L/2
Log
nth root
nth power
Inverse log
Log transformation
The log transformation maps a narrow range of low input grey level values into a wider range of output values
The inverse log transformation performs the opposite transformation

## Slide 17
Basic Gray Level Transformations
Log transformation
In Fourier transform, we usually encounter spectrum values that ranges from 0 to 106 or higher. But image display system cannot reproduce such a wide range of intensity values.
We usually set c to 1.
s = log(1 + r)
Original image
Fourier transform
Log transform of FT

## Slide 18
Image negatives
Log transformations
Power-law (Gamma) transformations
Piecewise Linear Transformation
Basic Gray Level Transformations

## Slide 19
Basic Gray Level Transformations
Power-law (Gamma) transformations
L-1
Input gray level r
Output gray level s
0
L/2
L-1
L/2
2
4
s = c · r γ
Map a narrow range of dark input values into a wider range of output values or vice versa
Varying γ gives a whole family of curves

## Slide 20
Basic Gray Level Transformations
Power-law (Gamma) transformations
r = 0.4
r = 0.5
原始图像
r = 0.3
r = 0.2
r = 0.6

## Slide 21
Basic Gray Level Transformations
Power-law (Gamma) transformations
Original Image
r = 0.3
r = 1.6

## Slide 22
Basic Gray Level Transformations
Power-law (Gamma) transformations
r = 3
r = 1
Original Image
r = 0.6

## Slide 23
Basic Gray Level Transformations
Power-law (Gamma) transformations
Original image
The images to the right show a magnetic resonance (MR) image of a fractured human spine
The given image is pre-dominantly dark, so an expansion of gray levels are desirable. This can be accomplished with a power-law transformation with a fractional exponent.

## Slide 24
Basic Gray Level Transformations
Power-law (Gamma) transformations
s = r 0.4
s = r 0.6
s = r 0.3

## Slide 25
Basic Gray Level Transformations
Power-law (Gamma) transformations
Gamma Correction
Many of you might be familiar with gamma correction of computer monitors.
Problem is that display devices, print devices do not respond linearly to different intensities, and they respond according to a power law:
For CRT display, γ=1.8~2.5
Can be corrected using a power law transformation:

## Slide 26
Basic Gray Level Transformations
Power-law (Gamma) transformations
Gamma Correction
γ=2.5
γ=1/2.5=0.4

## Slide 27
Basic Gray Level Transformations
Power-law (Gamma) transformations
Gamma Correction
Prior Knowledge about gamma correction
  Varying the value of gamma correction changes not only the brightness, but also the ratio of red to green to blue.
Applications
  Internet
  Millions of people and millions of monitors
  Gamma represents an “average ”of the types of monitors and computer systems
  Scanners, Printers have different values of gamma

## Slide 28
Image negatives
Log transformations
Power-law (Gamma) transformations
Piecewise Linear Transformation
Basic Gray Level Transformations

## Slide 29
Basic Gray Level Transformations
Piecewise Linear Transformation
Rather than using a well defined mathematical function we can use arbitrary user-defined transforms
The images below show a contrast stretching linear transform to add contrast to a poor quality image
？

## Slide 30
Basic Gray Level Transformations
Piecewise Linear Transformation
(r1,s1)=(rmin,0)
(r2,s2)=(rmax,L-1)
r1=r2=m

## Slide 31
Basic Gray Level Transformations
Piecewise Linear Transformation
Gray image
Original image
PLT
L-1
Input gray level r
Output gray level s
0
L/2
L-1
L/2
PLT

## Slide 32
Basic Gray Level Transformations
Piecewise Linear Transformation
L
x
0
a
b
ya
yb

## Slide 33
PART 2
Histogram Processing

## Slide 34
Histogram Processing
Definition
– The histogram function is defined over all possible intensity levels.
– For each intensity level, its value is equal to the number of the pixels with that intensity.
Applications
– Image enhancement, compression, segmentation
– Very popular tool for real time image processing
Image
Histogram
0 50 100 150 200 250 300
2500
2000
1500
1000
500
0

## Slide 35
Histogram Processing
0 1 2 3 4 5 6 7
Image 5x5

## Slide 36
Histogram Processing
Histogram
Image

## Slide 37
Histogram Processing
Histogram
Image

## Slide 38
Histogram Processing
Histogram
Image

## Slide 39
Histogram Processing
Dark Image
Bright Image
High Contrast
Low Contrast
It is reasonable to conclude that an image whose pixels tend to occupy the entire range of possible gray levels and, in addition, tend to be distributed uniformly, will have an appearance of high contrast and will exhibit a large variety of gray tones, thus will be an image that shows a great deal of gray-level detail and has high dynamic range.

## Slide 40
Histogram Processing
Histogram equalization
s=T(r) 0≤r≤L-1
  T is single-valued and monotonically increasing
  s is value-limited in [0,L-1]

## Slide 41
Histogram Processing
Histogram equalization
PDF relation between ps and pr
If the cumulative distribution function is used as the transform
then the PDF of the transformed image is

## Slide 42
Histogram Processing
Histogram equalization
Transform function
is the probability density function (pdf)
The transform function is the cumulative distribution function (CDF)
Why ? To make the pdf of the transformed image uniform, i.e., to make the histogram of the transformed image uniform.

## Slide 43
Histogram Processing
Histogram equalization
HE - discrete form
HE steps
  G – Number of gray levels, N – Number of pixels
  Calculate the histogram H[r], r=0,2,…G-1
  Normalize the histogram H[r] = H[r]/N;
  Form the CDF: Hc[0] = H[0], Hc[r] = Hc[r-1] + H[r]
  Set s = T[p] = round (Hc[p] (G-1))

## Slide 44
Histogram Processing
Histogram equalization
Example
Do histogram equalization on the 5x5 image with integer intensities in the range between one and eight
PDF r
p(r0) = 8/25 = 0.32
p(r1) = 4/25 = 0.16
p(r2) = 3/25 = 0.12
p(r3) = 2/25 = 0.08
p(r4) = 2/25 = 0.08
p(r5) = 0/25 = 0.00
p(r6) = 1/25 = 0.04
p(r7) = 5/25 = 0.20
Intensity
transformation function
T(r0) = 0.32*7
T(r1) = (0.32+0.16)*7=0.48*7
T(r2) = (0.32+0.16+0.12)*7=0.60*7
T(r3) = (0.32+0.16+0.12+0.08)*7=0.68*7
T(r4) = … = 0.76*7
T(r5) = … = 0.76*7
T(r6) = … = 0.80*7
T(r7) = … = 1.00*7
Histogram value
after HE
s0 = 2.24 → 2
s1 = 3.36 → 3
s2 = 4.42 → 4
s3 = 4.76 → 5
s4 = 5.32 → 5
s5 = 5.32 → 5
s6 = 5.60 → 6
s7 = 7.00 → 7

## Slide 45
Histogram Processing
Histogram equalization

## Slide 46
Histogram Processing
Histogram equalization

## Slide 47
Histogram Processing
Histogram equalization

## Slide 48
Histogram Processing
Histogram equalization
Adaptive histogram equalization:
Properties
The size of the neighborhood region is a parameter of the method. It constitutes a characteristic length scale: contrast at smaller scales is enhanced, while contrast at larger scales is reduced.
When the image region containing a pixel's neighborhood is fairly homogeneous, its histogram will be strongly peaked, and the transformation function will map a narrow range of pixel values to the whole range of the result image. This causes AHE to over amplify small amounts of noise in largely homogeneous regions of the image.
Must limit contrast expansion in flat regions of the image, e.g. by clipping individual histogram values to a maximum (CLAHE - “Contrast-limited adaptive histogram equalization”) [Pizer, Amburn et al. 1987]

## Slide 49
Histogram Processing
Histogram equalization
Original image
Adaptive histogram equalization:
Global histogram equalization
Adaptive histogram equalization
3×3

## Slide 50
Histogram Processing
Histogram equalization
Original image
Adaptive histogram equalization:
Global histogram equalization
Adaptive histogram equalization
8×8
Adaptive histogram equalization
32×32

## Slide 51
Histogram Processing
Histogram equalization
Adaptive histogram equalization:
Global histogram equalization
Adaptive histogram equalization
16×16
Original image
Dental Xray

## Slide 52
Histogram Processing
Histogram equalization
Adaptive histogram equalization:
Original image
Global histogram equalization
Adaptive histogram equalization
8×8

## Slide 53
PART 3
Arithmetic/Logical Operation

## Slide 54
Logic Operations
Image Subtraction
Image Averaging
Arithmetic/Logical Operation
Logic Operations

## Slide 55
Arithmetic/Logical Operation
Logic Operations
AND
OR

## Slide 56
Logic Operations
Image Subtraction
Image Averaging
Arithmetic/Logical Operation
Logic Operations

## Slide 57
Arithmetic/Logical Operation
Image Subtraction
f and h are two images.
Note: most images are displayed using 8 bits (even 24-bit color images consists of three 8 bit channels). Thus we expect image values not to be outside the range from 0 to 255.
In subtraction, the results should be in the range -255 to 255. so some sort of scaling is required to display the results.
Add 255 and then divide by 2
y=x-min(x); z=y*255/max(y).

## Slide 58
Arithmetic/Logical Operation
Image Subtraction
（Digital Subtraction Angiography，DSA）

## Slide 59
Arithmetic/Logical Operation
Image Subtraction
Enhancement by image subtraction.
(a) Mask image. (b) An image (taken after injection of a contrast medium into the bloodstream) with mask subtracted out.
（a）
（b）

## Slide 60
Arithmetic/Logical Operation
Image Subtraction
Change detection is another major application by using image subtraction. Such as:
Tracking moving vehicles
Tracking walking persons
Change detections

## Slide 61
Arithmetic/Logical Operation
Image Subtraction

## Slide 62
Arithmetic/Logical Operation
Image Subtraction
Two consecutive frames

## Slide 63
Arithmetic/Logical Operation
Image Subtraction
Image after thresholded
Simple difference image thresholded
Simple difference image

## Slide 64
Arithmetic/Logical Operation
Image Subtraction
Image A (no defect)
Image B (with defect)
A – B (alignment)
A – B (alignment and thresholding)

## Slide 65
Logic Operations
Image Subtraction
Image Averaging
Arithmetic/Logical Operation
Logic Operations

## Slide 66
Arithmetic/Logical Operation
Image Averaging
A noisy image:
Then Averaging M different noisy images can reduce the noise:
Where n(x) is the noise, and it has zero average value
As M increases, the variability of the pixel values at each location decreases.
  ---- This means that g(x,y) approaches f(x,y) as the number of noisy images used in the averaging process increases.
)
,
(
)
,
(
2
)
,
(
)
,
(
2
1
1
y
x
n
y
x
g
y
x
n
y
x
g
M
M
s
d
s
d
=
=

## Slide 67
Arithmetic/Logical Operation
Image Averaging
1 image
2 images
4 images

## Slide 68
Arithmetic/Logical Operation
Image Averaging
Image of Galaxy Pair NGC3314.
Image corrupted by additive Gaussian noise with zero mean and a standard deviation of 64 gray levels.
-(f)Results of averaging K = 6, 16, 64, and 128 noisy images.

## Slide 69
Arithmetic/Logical Operation
Image Averaging
(a) From top to bottom: Difference images between the images (a) and image (c)-(f) in the last figure, respectively.
(b) Corresponding histograms

## Slide 70
PART 4
Spatial Filtering

## Slide 71
Fundamentals (Kernel, convolution, filtering)
Smoothing (Linear / non-linear filters)
Sharpening (The Laplacian-2ndorder derivatives, the gradient -first order derivatives)
Combing Spatial Enhancement Methods
Spatial Filtering

## Slide 72
Spatial Filtering
Spatial Filtering
Images contain noise – sources sensor quality, light fluctuations, quantization effects

## Slide 73
Spatial Filtering
Spatial Filtering
Motivation: Image denoising
How can we reduce noise in a photograph?

## Slide 74
Spatial Filtering
Spatial Filtering
Given a noisy image
  How do we reduce noise ?
  How do we find useful features ?

## Slide 75
Spatial Filtering
Spatial Filtering
In this lecture we will look at spatial filtering techniques:
  – Neighborhood operations
  – What is spatial filtering?
  – Smoothing operations
  – What happens at the edges?
  – Correlation and convolution
  – Sharpening filters
  – Combining filtering techniques

## Slide 76
Spatial Filtering
Spatial Filtering
Given
–an image
–A neighborhood (typically a small rectangle)
–A predefined operation that is performed on the image pixel encompassed by the neighborhood
One of the most important tools in image / signal processing

## Slide 77
Spatial Filtering
Spatial Filtering
a r +b s +c t+
d u + f w +
g x + h y +i z
e
Original Image f ( x, y )
x
y
0
*
a b c
d e f
g h i
3×3 neighborhoods
r s t
u v w
x y z
3×3 mask
Filtered Image g ( x, y )
x
y
0
E

## Slide 78
Spatial Filtering
Spatial Filtering
At the edges of an image we are missing pixels to form a operation neighborhood

## Slide 79
Spatial Filtering
Spatial Filtering
Original Image
Filtered Image:
Zero Padding
Filtered Image:
Replicate Edge Pixels
Filtered Image:
limit the mask center to a distance from the border

## Slide 80
Fundamentals (Kernel, convolution, filtering)
Smoothing (Linear / non-linear filters)
Sharpening (The Laplacian-2ndorder derivatives, the gradient -first order derivatives)
Combing Spatial Enhancement Methods
Spatial Filtering

## Slide 81
Spatial Filtering
Smoothing
• What are they for ?
  Smoothing linear spatial filters are used for blurring and / or for noise reduction
  Filter coefficients are positive
  They are sometimes called
    averaging filters
    Lowpass filters:
      Because noise is in the high-frequencies of the signal, noise removal consists of filtering out high frequencies of the signal

## Slide 82
Spatial Filtering
Smoothing
One of the simplest spatial filtering operations we can perform is a smoothing operation
Simple averaging filter
– Simply average all of the pixels in a neighborhood around a central value
– Especially useful in removing noise from images
– Also useful for highlighting gross detail

## Slide 83
Spatial Filtering
Smoothing
e
原始图像 f ( x, y )
x
y
0
=
=101.222
*
滤波后图像 g ( x, y )
x
y
0
E
3×3模板
3×3邻域
102
96
97
103
98
105
102
The above is repeated for every pixel in the original image to generate the smoothed image.

## Slide 84
Spatial Filtering
Smoothing

## Slide 85
Spatial Filtering
Smoothing
More effective smoothing filters can be generated by allowing different pixels in the neighborhood with different weights in the averaging function
Weighted averaging filter
– It is called weighted average
– Pixels at the center of the mask are multiplied with high values gives to the pixel more importance.
– The other pixels are inversely weighted as a function of their distance to the center.
– This aims at reducing blurring in the smoothing process

## Slide 86
Spatial Filtering
Smoothing
The image at the top left is an original image of size 500*500 pixels
The subsequent images show the image after filtering with an averaging filter of increasing sizes 3, 5, 9, 15 and 35
Notice how detail begins to disappear
Effects of the filter size

## Slide 87
Spatial Filtering
Smoothing
Why blurring an image ?
Obtain a gross representation of objects of interest:
  intensity of small objects blends with background
  Large objects become “blob-like”
The size of the filter mask establishes the relative size of the objects that will be blended with the background

## Slide 88
Spatial Filtering
Smoothing
Example of application
– Detecting important objects in an image
(left) Image from hubble telescope. (center) Filtered with a 15x15 averaging mask. (right) Result of thresholding the image in the center
(25%*max(g))

## Slide 89
Spatial Filtering
Smoothing
How big should the mask be?
The bigger the mask,
– more neighbors contribute.
– smaller noise variance of the output.
– bigger noise spread.
– more blurring.
– more expensive to compute.

## Slide 90
Spatial Filtering
Smoothing
Limitations of averaging
  Signal frequencies shared with noise are lost, resulting in blurring.
  Impulsive noise is diffused but not removed.
  It spreads the noise, resulting in blurring.

## Slide 91
Spatial Filtering
Smoothing
Order-Statistics Filters
Order-statistics filters (also referred to as rank order filters) are nonlinear spatial filters whose response is based on ordering (ranking) the pixels contained in the image area encompassed by the filter, and then replacing the value of the center pixel with the value determined by the ranking result.
Types: median filter, max filter, min filter

## Slide 92
Spatial Filtering
Smoothing
Median Filter
In order to perform median filtering at a point in an image, we first sort the values of the pixel in question and its neighbors, determine their median, and assign this value to that pixel.
Several types of the window
· · · · ·
· · · · ·
· · · · ·
· · · · ·
· · · · ·
·
· · ·
· · · · ·
· · ·
·
·
·
· · · · ·
·
·
· · ·
· · ·
· · ·
·
· · ·
·

## Slide 93
Spatial Filtering
Smoothing
x[n] | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2
x[n] | 1 | 3 | 1 | 1 | 1 | 2 | 3 | 2 | 2 | 3
x[n] | - | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | -
x[n] | - | 1.7 | 1.7 | 1 | 1.3 | 2 | 2.3 | 2.3 | 2.2 | -
Edge
The edge is smoothed
Example
Impulse noise
Median
(N=3)
Average
(N=3)
Median Filter

## Slide 94
Spatial Filtering
Smoothing
Original Image With Salt and Pepper Noise
Image After Averaging Filter (3×3)
Image After Median Filter (3×3)
Median Filter

## Slide 95
Spatial Filtering
Smoothing
3×3
Image with salt and pepper noise
5×5
7×7

## Slide 96
Thanks