## Slide 1
Machine Vision
Wu Wei

## Slide 2
01
Arithmetic/Logical Operation
Gray Level Transformations
Histogram Processing
Images Enhancement
02
03
Spatial Filtering
04
Frequency Filtering
05

## Slide 3
Spatial Filtering
Smoothing
Original
Filtered (no change)

## Slide 4
Spatial Filtering
Smoothing
Original

## Slide 5
Spatial Filtering
Smoothing
Original
Shifted left By 1 pixel

## Slide 6
Spatial Filtering
Smoothing
Original

## Slide 7
Spatial Filtering
Smoothing
Original
Blur (with a box filter)

## Slide 8
Spatial Filtering
Smoothing
Original
(Note that filter sums to 1)

## Slide 9
Fundamentals (Kernel, convolution, filtering)
Smoothing (Linear / non-linear filters)
Sharpening (The Laplacian-2ndorder derivatives, the gradient -first order derivatives)
Combing Spatial Enhancement Methods
Spatial Filtering

## Slide 10
Spatial Filtering
Sharpening
Principle objective
To highlight fine detail in an image or to enhance detail that has been blurred, either in error or as a natural effect of a particular method of image acquisition.

## Slide 11
Spatial Filtering
Sharpening
Previously we have looked at smoothing filters which remove fine detail
Sharpening spatial filters seek to highlight fine detail
  - Remove blurring from images
  - Highlight edges
Sharpening filters are based on spatial differentiation
Image
Sharpened image

## Slide 12
Spatial Filtering
Sharpening
  Properties of 1st and 2nd-Order Derivatives
  Use of 2nd Derivatives for Enhancement- The Laplacian
  Use of 1st Derivatives for Enhancement - The Gradient

## Slide 13
Spatial Filtering
Sharpening
First order derivative for a discrete function
Second order derivative for a discrete function

## Slide 14
Spatial Filtering
Sharpening
8 | 8 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | 0 | 0 | 1 | 4 | 1 | 0 | 0 | 0 | 9 | 0 | 0 | 5 | 5
 | 0 | 0 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | -1 | 0 | 0 | 1 | 3 | -3 | -1 | 0 | 0 | 9 | -9 | 0 | 5 | 0
 | 0 | -1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 2 | -6 | 2 | 1 | 0 | 9 | -18 | 9 | 5 | -5 | 
Gray level profile
Image strip
First Derivative
Second Derivative

## Slide 15
Spatial Filtering
Sharpening
Definition:
First derivative filter output
  Zero at constant intensities
  Non zero at the onset of a step or ramp
  Non zero along ramps
Second derivative filter output
  Zero at constant intensities
  Non zero at the onset of a step or ramp
  Zero along ramps
First derivative filter output
Second derivative filter output

## Slide 16
Spatial Filtering
Sharpening
Conclusion:
First-order derivatives generally produce thicker edges in an image.
Second-order derivatives have a stronger response to fine detail, such as thin lines and isolated points.
First order derivatives generally have a stronger response to a gray-level step.
Second-order derivatives produce a double response at step changes in gray level.

## Slide 17
Spatial Filtering
Sharpening
  Properties of 1st and 2nd-Order Derivatives
  Use of 2nd Derivatives for Enhancement- The Laplacian
  Use of 1st Derivatives for Enhancement - The Gradient

## Slide 18
Spatial Filtering
Sharpening
A common second derivative sharpening filter is the Laplacian
– Isotropic
• Rotation invariant: Rotating the image and applying the filter is the same as applying the filter and then rotating the image.
– One of the simplest sharpening filters

## Slide 19
Spatial Filtering
Sharpening
The Laplacian

## Slide 20
Spatial Filtering
Sharpening
8
4
4
8
-
The Laplacian

## Slide 21
Spatial Filtering
Sharpening
10
Laplacian Filtered Image
Original Image
The Laplacian

## Slide 22
Spatial Filtering
Sharpening
The result of a Laplacian filtering is not an enhanced image
  We have to do more work
  Subtract the Laplacian result from the original image to Laplacian Filtered Image generate our final sharpened enhanced image
The Laplacian

## Slide 23
Spatial Filtering
Sharpening
The Laplacian
-
=
In the final, sharpened image, edges and fine detail are much more obvious

## Slide 24
Spatial Filtering
Sharpening
The Laplacian
Original Image
Enhanced Image

## Slide 25
Spatial Filtering
Sharpening
The Laplacian
Original Image
Enhanced Image

## Slide 26
Spatial Filtering
Sharpening
The Laplacian
if the center coefficient of the Laplacian mask is negative
if the center coefficient of the Laplacian mask is positive
The composed Laplacian enhancement image is given by:
8
4
4
8
-

## Slide 27
Spatial Filtering
Sharpening
The Laplacian
The entire enhancement can be combined into a single filtering operation:

## Slide 28
Spatial Filtering
Sharpening
The Laplacian
This gives us a new filter which does the whole job in one step

## Slide 29
Spatial Filtering
Sharpening
The Laplacian
There are lots of slightly different versions of the Laplacian that can be used:

## Slide 30
Spatial Filtering
Sharpening
The Laplacian
Original
(Note that filter sums to 1)
Sharpening filter
- Accentuates differences with local average

## Slide 31
Spatial Filtering
Sharpening
The Laplacian
Before
After

## Slide 32
Spatial Filtering
Sharpening
The Laplacian
Unsharp Masking and High-Boost Filtering
Unsharp masking is expressed as
where is a blurred version of f(x, y)
high-boost filtering ---- a slight further generalization of unsharp masking

## Slide 33
Spatial Filtering
Sharpening
  Properties of 1st and 2nd-Order Derivatives
  Use of 2nd Derivatives for Enhancement- The Laplacian
  Use of 1st Derivatives for Enhancement - The Gradient

## Slide 34
Spatial Filtering
Sharpening
The Gradient -Use of 1st Derivatives for Enhancement
  They are implemented using the magnitude of the gradient
    –Gradient definition
    –The magnitude of the Gradient
    – For computational consideration, in practice
Notes: ，

## Slide 35
Spatial Filtering
Sharpening
The Gradient
The gradient points in the direction of most rapid increase in intensity.

## Slide 36
Spatial Filtering
Sharpening
The Gradient
Which shows changes with respect to x?
Original Image
fy
fx

## Slide 37
Spatial Filtering
Sharpening
The Gradient
Sobel operator (filter) is a popular discretization of the gradient
– fx is calculated using Tx, and fy using Ty
  – The magnitude of the gradient is then given by:

## Slide 38
Spatial Filtering
Sharpening
The Gradient
Original Image
fx
fy
Gradient Image

## Slide 39
Spatial Filtering
Sharpening
The Gradient

## Slide 40
Spatial Filtering
Sharpening
The Gradient
Original Image
Gradient Image
Sobel operator
Roberts Cross operator
Prewitt operator
Scharr operator

## Slide 41
Spatial Filtering
Sharpening
The Gradient
Input image Gradient magnitude
Sobel gradient aids to eliminate constant or slowly varying shades of gray and assist automatic inspection.
It also enhances small discontinuities in a flat gray filed.
(at four
and five o’clock in the image)

## Slide 42
Fundamentals (Kernel, convolution, filtering)
Smoothing (Linear / non-linear filters)
Sharpening (The Laplacian-2ndorder derivatives, the gradient -first order derivatives)
Combing Spatial Enhancement Methods
Spatial Filtering

## Slide 43
Spatial Filtering
Combing Spatial Enhancement
Successful image enhancement is typically not achieved using a single operation
Rather we combine a range of techniques in order to achieve a final result
This example will focus on enhancing the bone scan to the right
The narrow dynamic range of the low gray levels and high noise content make this image difficult to enhance.

## Slide 44
Spatial Filtering
Combing Spatial Enhancement
Utilize the Laplacian to highlight fine detail
Utilize the gradient to enhance prominent edges
Combine Laplacian and smoothed gradient to get the detail-enhanced and noise-compressed image
Increase the contrast of low gray levels by using a gray-level transformation.

## Slide 45
Spatial Filtering
Combing Spatial Enhancement
A rather noisy sharpened image is expected.
Laplace operator
Original image

## Slide 46
Spatial Filtering
Combing Spatial Enhancement
mask image
5 x 5 box smooth

## Slide 47
Spatial Filtering
Combing Spatial Enhancement
add to the
original
sharpen enhanced image
strong edges and the relative lack of visible noise
Laplacian
enhanced
smoothed
Sobel
gradient
sharpened image

## Slide 48
Spatial Filtering
Combing Spatial Enhancement
Compare the original and final images
γ=0.5 c=1

## Slide 49
Thanks